## Slide 1: Core dumps
What Is It? Where? What to Do?

## Slide 2: Core Dump – What IS IT?
A file produced by the OS when the application tries to access an address outside that allocated to the application.
Usually the result of a programming error of some kind.
The offending application disappears and no longer functions. If the application was ‘critical’, the watchdog will shut the system down.

## Slide 3: Core Dumps – where?
A core dump file is generated by the OS and will be located in the /data/errors/ directory.
File name begins with the application name followed by ‘core’
example gp_test-core-11.25151
Most CyFlex systems have a ‘cleanup’ process that is defined by the ‘usercron’ specification file. This will normally delete the core dump files after 2 weeks, but usercron can be modified to extend that time period. Evidence of the incident is lost after that period of time.

## Slide 4: Core Dumps – what TO DO?
Core dump files can be analyzed by a debugger provided that the source code is available.
Source code is not usually available at a test site but can be installed there by a TRP Labs developer.
The debugger will usually show the developer the source code file and lines of code where the fault occurred.

## Slide 5: Core DUMP – What TO DO?
C-language source code shown by the debugger is usually only useful to the developers who wrote the application or are familiar with the CyFlex design.
Submit a JIRA issue to TRP Labs with the following information.
  the application name
  location (site, tc#, IP address).
  any recent action or spec file change that might have caused the dump

## Slide 6: Core DUMP – What TO DO?
A checking program is available to monitor a system for core dumps and produce an email message if any appear. Contact TRP Labs for installation.