## Slide 1: CyFLex Driver improvements
What to expect

## Slide 2: DriverS In the past
Driver update rates in prior CyFlex versions were based on the 'ai_transfer' tasks and what the channel rates were specified as in the inpt_specs files.
Some drivers such as 'snapio' were hard coded to limit transfer rates to 10hz
Transfer of driver data to the transfer layer was based on multiple timers.

## Slide 3: Pitfalls of the past
Because the drivers had multiple timers involved, this could lead to update delays to channel values.
Channels values were waiting on CyFlex rather than waiting on the devices.
If the device is controlling something, the update delay should be minimized.

## Slide 4: CyFLex Driver improvements
The CyFlex drivers have now been updated to improve performance.
Instead of being timer driven, tasks are now signaled directly. As soon as a device sends a new value to a channel, it will update immediately.
Hard coded rate limitations of the drivers have been removed. Update rates are now dependent on the device capabilities.

## Slide 5: How much did the improvements help?
Comparison of improvements are based on round trip time.
Ex: CyFlex sets an AO value to the device, then the AO channel on the device is connected to an AI channel on the same device. How long it took CyFlex to see the AI value change when the AO was set is the time being measured.

## Slide 6: How much did the improvements help?
Old Drivers
    Snapio driver: ~105 milliseconds, ~9.5HZ
    Eblox driver: ~56 milliseconds, ~17.8HZ
New Drivers
    Snapio driver: ~56 milliseconds, ~17.8HZ
    Eblox driver: ~26 milliseconds, ~38HZ
Snapio became ~46.6% faster and Gantner became ~54% faster

## Slide 7: What it affects
The improvements affect the following drivers:
    Gantner/Eblox
    Snapio
    Cyrius
    Ecat/Ethercat
    Modbus
It does NOT affect:
    Analog outputs and digital outputs
    Serial tasks (devcom, gmodbus, AK, etc.)

## Slide 8: What needs to be done
Nothing! When upgrading to CyFlex 6.3.0, the driver improvements will all be active.
With the increased performance of the input channels, you may want to modify 'ao_transfer' and 'do_logi_xfer' tasks in the go.scp, as you may be able to increase the rates for better response. The rates should be just as high as the rates for your 'ai_transfer' task.

## Slide 9: Other considerations
The ethercat driver is relatively new and is useable. It has been in older versions, and was mainly for testing, but improvements continue to be made for it. It is faster than general TCP/IP and many new devices are adding this protocol for communication. A few testcells have made use of it, and can even be used with Gantner devices.
There is also a new modbus driver. It uses the modbus protocol like gmodbus, but has all the benefits of a driver such as calibration tables.
If interested with either of the above, contact us for assistance.