## Slide 1: Cyflex Diagnostic tools

## Slide 2: Diagnostic Tools
Some diagnostic tools have been designed for developers and support personnel and don’t have good documentation
Most diagnostic tools are rarely used
When a problem occurs customers may be asked by a developer to run one of the diagnostics and capture the output

## Slide 3: Diagnostic Tools
“events” – monitor selected events
“evnt_info” – show existing events and event attachments
Error messages – message formats, “errs”, “errc”
“show_mem” – allocation of re-sizeable memory areas and event allocation
“ms_diag” – shows applications attached to standard process intervals

## Slide 4: Diagnostic Tools
“gp_test” trace files – log of sequence of modal transitions
“evnt_rsp” trace files – log of input events and output actions
Compressed history – future session

## Slide 5: “events”
Enter one or more existing event names followed by a period “.”
Every occurrence of those events will be logged to the console
Output includes event_name, event_id, time_stamp, sending application name and process ID

## Slide 6: “events”
Type in event name followed by <Enter.>
Enter a period "." to end list.
event_name event_id hex/dec date time sender pid,name
auSTR79b0-114 20002d4/33555156 09/03/19 12:28:13.394 pid=31152,gp_test
auRPL79b0-114 20002d6/33555158 09/03/19 12:28:13.395 pid=31843,vrbl_to_file
auSTR79b0-114 20002d4/33555156 09/03/19 12:28:26.411 pid=31152,gp_test
auRPL79b0-114 20002d6/33555158 09/03/19 12:28:26.412 pid=31843,vrbl_to_file
advance_mode 2000010/33554448 09/03/19 12:28:32.798 pid=7671,adv
auSTR79b0-114 20002d4/33555156 09/03/19 12:28:35.801 pid=31152,gp_test
auRPL79b0-114 20002d6/33555158 09/03/19 12:28:35.801 pid=31843,vrbl_to_file
auSTR79b0-114 20002d4/33555156 09/03/19 12:28:48.827 pid=31152,gp_test
auRPL79b0-114 20002d6/33555158 09/03/19 12:28:48.827 pid=31843,vrbl_to_file
new_test 2000008/33554440 09/03/19 12:28:52.451 pid=7673,

## Slide 7: “evnt_info”
Show all event names currently in the system
Show all applications currently attached to any event
Show all applications that are attached to a particular event
Show all event attached by a particular application
Show event queue for an event
Tally last 100 events

## Slide 8: “error messages”
“errs” command shows current log of error messages
Error messages, in some cases, may also appear on the console
Error 43 in Task: limit_specs TID:6034(24628) On 09:15:43-Sep 04
File: /cyflex.6.3.exp/limits/limit_specs.c Line: 822
variable label <xerra109_1> not found -line 410

## Slide 9: “error messages”
Error 43 in Task: limit_specs TID:6034(24628) On 09:15:43-Sep 04
File: /cyflex.6.3.exp/limits/limit_specs.c Line: 822
variable label <xerra109_1> not found -line 410
Error 43 in Task: limit_specs TID:6034(24628) On 09:15:43-Sep 04
^err_code ^application ^process ID ^time
File: /cyflex.6.3.exp/limits/limit_specs.c Line: 822
^source code file & line #
variable label <xerra109_1> not found -line 410
^ a configurable line of information that should be helpful to the user

## Slide 10: “error messages”
“errc 43”- may offer longer and better explanation of the problem
Error string = LABEL_NOT_FOUND, error value = 43
This value is returned from find_real_label(), find_logical_label(),
find_integer_label(), when they are not successful in locating the
label string. These routines are used to associate a channel label
with an REAL_VARIABLE, LOGICAL_VARIABLE, or INTEGER_VARIABLE. In other
words, if the user types in a channel label like "blowby", these routines
are used to find the blowby channel. In the case of this example it
would be a REAL_VARIABLE and an analog input channel. Usually the user
has made a typing error, but it may be that the channel was not specified
in inpt_specs.nnn, di_specs.nnn, do_specs.nnn, perf_labels.nnn, and isn't
an internally generated label. (nnn == test cell number )

## Slide 11: “error messages”
“errc -279”- may offer longer and better explanation of the problem
a) This error code is returned when the event adm has reached
its limit of events that can be created, regardless of what kind of event
is trying to be created. The maximum number of events is a spawning
argument for the event adm. The maximum number of events can be
determined by entering the command 'sin -Pevnt_adm'. If the maximum
number of events (the 1st spawning argument) is the same as the number of
events already in existence (determined by running evnt_info) then
event adm should be restarted with a larger number of maximum events.
This will require modification of the /cell/go.scp file and running
a "go" command, which restarts the entire CyFlex system and should not
be done while the test object (engine) is running.

## Slide 12: “error messages”
“errc -279”- may offer longer and better explanation of the problem
b) Attempt to create a timer event has failed. Most likely cause is an
invalid parameter, such as the time interval specified. Another cause
maybe that the total number of timers allowed by the system has been
reached.
*

## Slide 13: “evnt_rsp trace file”
The “evnt_rsp” process logs all incoming events and resulting actions to file in /ram/ named “er_trace.<instance>
When 100 events have been logged, the file is copied to the /data/errors/ directory with a timestamp appended to the file name. Then the logging in /ram/ starts over.

## Slide 14: “evnt_rsp trace file”
EvntResp: Received event-<UDPTimestampErr> from <17949/eblox_srvr> at 09:11:40 09/04/19
<door_is_open> set to <0>
EvntResp: Received event-<fr_done> from <18905/datapoint> at 09:11:47 09/04/19
IF_TRUE <Engine_Run> passed
IF_TRUE <SpeedGT400> passed
IF_TRUE <enab_lwr_lmt> failed
IF_TRUE <FR_in_prg> failed
IF_TRUE <FR_request> failed
IF_FALSE <Engine_Run> failed
IF_FALSE <Safety_Trip> passed
IF_FALSE <gp_trace> failed
IF_FALSE <gen_labels_diag> passed

## Slide 15: “gp_test trace file”
The “gp_test” process will log mode changes to a file if configured to do so in the “gp_header” file
@TRACE_FILENAME keyword specifies the file and maximum number of mode changes before the file is saved as a backup and restarted
@TRACE_FILENAME
  /specs/gp/TRACE 1000
@TRACE_ENABLE keyword specifies a flag variable and initial state to enable/disable trace file entries
@TRACE_ENABLE
  gp_trace ON

## Slide 16: “gp_test trace file”
'1567593759' mode 0 terminated at- 09/04/19 06:42:39.575
nt command - /specs/gp/gp_wdl_SRC
gp_wdl_SRC,1 | Initialize Variables
'1567593769' mode 1 terminated at- 09/04/19 06:42:49.615
timeout - 10[sec]
gp_wdl_SRC,3 | Start Logger Task
'1567593769' mode 3 terminated at- 09/04/19 06:42:49.715
timeout - 0.1[sec]

## Slide 17: “gp_test trace file”
gp_wdl_SRC,5 :2/5000 | Start Logging and switch modes
'1567593769' mode 5 terminated at- 09/04/19 06:42:49.815
timeout - 0.1[sec]
gp_wdl_SRC,10 | Set Start Time
'1567593769' mode 10 terminated at- 09/04/19 06:42:49.815
immediate -
gp_wdl_SRC,14 | Read in setpoint info
'1567593769' mode 14 terminated at- 09/04/19 06:42:49.815
AUXILIARY_TASK - auRPL4a4f-114 - success

## Slide 18: “gp_test trace file”
gp_wdl_SRC,300 | Call return
'1567593769' mode 300 terminated at- 09/04/19 06:42:49.815
PROCEDURE called - return
return,10 | Test return
'1567593769' mode terminated at- 09/04/19 06:42:49.825
.01[sec] - RETURN to /specs/gp/gp_wdl_SRC