## Slide 1: Hour Meters

## Slide 2: Hour METER VARIABLES
Cell_meter – running hours for test cell
runs if “hr_meter_run” is TRUE
or if “Test_hrs_acc” is TRUE
test_hrs – reset-able meter
runs if “Test_hrs_enab” is TRUE
and of either “hr_meter_run is TRUE
or “Tst_hrs_acc” is TRUE

## Slide 3
engine_hrs – reset-able meter
runs if “hr_meter_run is TRUE
hr_meter_run – flag indicates test object is running or active
runs if “hr_meter_th” value is exceeded by the
HOUR_METER_VARIABLE value

## Slide 4
hr_meter_th – threshold value for engine to be considered running
the value which must be exceeded by the
HOUR_METER_VARIABLE value
Tst_hrs_acc – flag used to force meters to run even when
the “hr_meter_run” flag is FALSE
Tst_hrs_enab – flag use to force “test_hrs” to accumulate
If either “hr_meter_run” or “Tst_hrs_acc” is TRUE

## Slide 5
HOUR_METER_VARIABLE Speed
The string "HOUR_METER_VARIABLE" is a function code entered in the “spcl_chans” file and must be spelled exactly as above. The string "Speed" is the label of the variable which will be used to sense that the engine is running. Normally, this is the engine speed, but it may be changed to oil pressure or other variables as appropriate.
The identification of the threshold value for the HOUR_METER_VARIABLE is done in the /cell/cell_special file. The parameter "hr_meter_th" sets the value of the threshold used to turn on the "hr_meter_run" flag.
Note that this variable must have the same units as the variable identified by the HOUR_METER_VARIABLE function code. An example line from the cell_special file is shown below for setting the threshold value to 100[rpm].
28 hr_meter_th rpm 0 100 OFF 1.0
^____value