## Slide 1: InterNODAL communications

## Slide 2
    CyFlex offers several applications that support rapid transfers of data from one system to another.
    Primary use is to share the value of a set of variables between systems.
    Supports complex functionality to be implemented by multiple cooperating computers.
    Supports sharing of centralized collection of facility-wide parameters such as barometer, combustion air duct humidity, fuel supply characteristics, natural gas composition, etc.
Internodal Communication

## Slide 3
    connsrvr – TCP/IP based data transfer mechanism
      CyFlex version-independent
      Supported on Linux, MS-Windows, QNX
      Requires a specification file (connsrvr_specs.<name>) to identify external nodes (IP addresses) that are supported
      SERVERS
        List of nodes that provide a service to this node through snode_link, push_link, getAstStat, etc.
      DYNAMIC_SERVERS
        list of domains allowed to request data from this node
Internodal Communication– connsrvr

## Slide 4
Internodal Communication– connsrvr_specs
# Connection Server Specfile
VERSION
1
# List remote nodes that provide a service to this node through # the connection server.
# Examples of the server are sm_server, small_sm and indicom.
# Examples of the applications requesting this service are # node_link, snode_link, and getAstStat.
# HOST NAMES or IP ADDRESS
SERVERS
# Host Remote
# NAME Server Port
ctcnode45 -
ctcnode206 -
ctcnode230 -
# Windows Indicom Server
10.2.1.100 -
$
# List up to 5 ip address masks that the connection_server will accept # ad-hoc requests from remote connection servers. These are remote # connection servers that need a service such as sm_server or indicom.
#
# DYNAMIC_SERVER RANGE
DYNAMIC_SERVERS
143.222.0.0
# Windows Indicom Dynamic_Server
10.2.1.0
$
SERVER_TIMEOUT
300
$

## Slide 5
    csdump – This is a diagnostic utility for the connection server, “connsrvr”
      A command line utility that takes a snapshot of current status of communication status
        csdump | less
      Output is a little cryptic, but it will show which nodes are communicating and whether there are networking errors
      Some documentation in user manual
Internodal Communication– csdump

## Slide 6
Internodal Communication– csdump.1
Local Attached Services:
sm_serv_MAR09 pid( 22780) ipaddr 0.0.0.0
sm_serv_FEB06 pid( 22778) ipaddr 0.0.0.0
LV_inter pid( 22779) ipaddr 0.0.0.0
sm_serv_MAR09 - push_server
sm_serv_FEB06 - small_sm
LV_inter_pid - web_sm_server

## Slide 7
Internodal Communication– csdump.2
Remote Attached Services:
sm_serv_MAR09 pid( 23642) ipaddr XXX.XXX.XXX.171
sm_serv_FEB06 pid( 23640) ipaddr XXX.XXX.XXX.171
indicom pid( 4196) ipaddr XXX.XXX.XXX.100
sm_serv_FEB06 pid( 18244) ipaddr XXX.XXX.XXX.86
LV_inter pid( 18276) ipaddr XXX.XXX.XXX.86
sm_serv_MAR09 pid( 3830) ipaddr XXX.XXX.XXX.65
sm_serv_FEB06 pid( 3829) ipaddr XXX.XXX.XXX.65
sm_serv_FEB06 pid( 32589) ipaddr XXX.XXX.XXX.41
sm_serv_FEB06 pid( 3012) ipaddr XXX.XXX.XXX.165
sm_serv_FEB06 pid( 3618) ipaddr XXX.XXX.XXX.36
sm_serv_FEB06 pid( 15741) ipaddr XXX.XXX.XXX.39
sm_serv_FEB06 pid( 3306) ipaddr XXX.XXX.XXX.107
LV_inter pid( 3308) ipaddr XXX.XXX.XXX.107
sm_serv_FEB06 pid( 3790) ipaddr XXX.XXX.XXX.98
sm_serv_FEB06 pid( 2977) ipaddr XXX.XXX.XXX.95
sm_serv_MAR09 pid( 2978) ipaddr XXX.XXX.XXX.95
sm_serv_FEB06 pid( 6078) ipaddr XXX.XXX.XXX.36

## Slide 8
Internodal Communication– csdump.3
Connected Remote Servers:
Alive Listen SendTo Msg Packet Error Last Send Requestor Msg Packet Error Last
Hostname/IP Time Taskid Taskid Count Count Count Time Taskid Taskid Count Count Count Time
XXX.XXX.XXX.171 09:24:40 27042 0 0 0 0 19:00:00 27043 0 0 0 0 19:00:00
XXX.XXX.XXX.86 09:24:40 23093 0 0 0 0 19:00:00 23094 0 0 0 0 19:00:00
XXX.XXX.XXX.153 09:24:40 23011 0 0 0 0 19:00:00 23012 0 0 0 0 19:00:00
XXX.XXX.XXX.65 09:25:45 20612 22778 907 43 0 09:26:32 20613 22778 878 90 0 09:26:32
XXX.XXX.XXX.44 09:26:02 20607 0 0 0 0 19:00:00 20608 0 0 0 0 19:00:00
XXX.XXX.XXX.41 09:26:31 20599 22779 612 807 28 08:51:41 20600 22779 584 13092 0 08:51:41
XXX.XXX.XXX.42 09:26:31 20597 0 0 0 0 19:00:00 20598 0 0 0 0 19:00:00
XXX.XXX.XXX.165 09:26:02 20595 0 0 0 0 19:00:00 20596 0 0 0 0 19:00:00
XXX.XXX.XXX.39 09:22:21 20449 22778 17 17 0 07:29:14 20450 22778 17 17 0 07:29:14
XXX.XXX.XXX.252 09:22:21 20447 0 0 0 0 19:00:00 20448 0 0 0 0 19:00:00
XXX.XXX.XXX.155 09:24:40 20445 0 0 0 0 19:00:00 20446 0 0 0 0 19:00:00
XXX.XXX.XXX.36 09:26:31 20443 0 0 0 0 19:00:00 20444 0 0 0 0 19:00:00
XXX.XXX.XXX.208 09:22:21 20441 0 0 0 0 19:00:00 20442 0 0 0 0 19:00:00
XXX.XXX.XXX.107 09:22:21 20439 22778 155259 155259 60 09:26:36 20440 22778 155199 155199 0 09:26:36
XXX.XXX.XXX.98 09:22:21 20437 22778 155259 155259 60 09:26:38 20438 22778 155199 155199 0 09:26:38
XXX.XXX.XXX.100 09:26:40 20342 6905 197679 197679 0 15:37:25 20357 6905 197714 197714 0 15:37:25
node230 09:24:40 20343 0 0 0 0 19:00:00 27009 0 0 0 0 19:00:00
node206 09:14:38 20344 0 0 0 0 19:00:00 27010 0 0 0 0 19:00:00
node45 09:24:41 20345 22807 25865 25865 0 09:26:05 27011 22807 25865 25865 0 09:26:05

## Slide 9
    small_sm– version-dependent application which is aware of the organization of shared memory on the local node
      Responds to a version-independent message from remote nodes
        Value
        Units
        Display format
        Last update time
      Supports communication with multiple remote nodes
      Supports only individual members of data types which contain multiple values (statistical, composition, etc.)
Internodal Communication–small_sm

## Slide 10
    small_smN – identical to sm_server except that it is designed to work exclusively with only one remote node to avoid contention with other nodes
      Launched with an argument to identify the remote service it supports
        small_smN em_cart &
      Remote node must run ‘node_linkN’ using the same identifier at the ‘extender’ optional argument
        node_linkN extender=em_cart &
Internodal Communication–small_smN

## Slide 11
    snode_link – Used mostly to fetch the value of variables from remote nodes, but can push values
      Supports multiple nodes
      Supports multiple instances
        Best to isolate high data rates (>1[hz])
      Arguments
        Specification filename
        name – unique registered name of this instance
        node=(tc_name) – overrides @HOSTNAME in first block
        host=hostname or IP address of remote system
        Direction=(push/pull) – default is ‘pull’
Internodal Communication–snode_link

## Slide 12
    node_linkN – Identical to snode_link except it communications with a remote instance of small_smN
      Supports multiple nodes
      Supports multiple instances
        Best to isolate high data rates (>1[hz])
      Arguments
        Specification filename
        name – unique registered name of this instance
        host=hostname or IP address of remote system
        extender=<identifier of the remote small_smN)
        Direction=(push/pull) – default is ‘pull’
Internodal Communication–node_linkN

## Slide 13
    push_server
      Supports transmissions from remote push_link instances
      Similar to small_sm, but only supports requests to set variable values rather than retrieve them
      Reduces network traffic as UDP message only flow in one direction – no response is required
      Launched without any arguments
        push_server &
    push_link
      similar to snode_link, but only supports requests to set variable values rather than retrieve them
      Launched with same arguments as snode_link
        push_link /specs/push_specs &
push_link/push_server

## Slide 14
  Used to send event messages to remote nodes.
  Does not use connsrvr.
  Not a fast connection
  Primary application if for ‘onga_onga’ messages containing natural gas concentration information
  Can be used to trigger some activity on a remote node by sending a signal event.
  ev_tcp_receive can be launched with an IP mask to filter requestors
    ev_tcp_receive XXX.XXX.XXX.65
ev_tcp_send/ev_tcp_receive/ev_tcp_specs

## Slide 15
# the source_event_name is the event name on the network where the # event is being "set".
#This must be the same network on which # spec file is being processed.
# the destination_event_name is the event name on the network where the event is received
# node320
# destination source_event_name destination_event_name
XXX.XXX.XXX.168 onga_onga onga_onga
# node115
# destination source_event_name destination_event_name
XXX.XXX.XXX.109 onga_onga onga_onga
# destination source_event_name destination_event_name
node16 start_it at_speed
nodeqnx release_it pier_done
ev_tcp_specs file format

## Slide 16
getAstStat13 – service that normally runs only on central node
  Uses /data/cell_map file to determine a list of nodes from which it will fetch the following values
  hour, test_hrs, total_work, abs_work, mot_work, eng_hrs, total_fuel, last_on_time, last_off_time, util_7day, go_count, down_code, run, eng_Model, sn, test_type, engineer, technician, Test_ID, prog_proj
  No specification file is required
  Variables are automatically created
  Variables are automatically added to the “save_list”
  Variables are logged to /data/meters/meterlog.<cell_name> by the “meterlogall” application at 0:00, 07:00, 16:00, 23:00
getAstStat13

## Slide 17
getAstStatGen – identical to getAstStat13 except that variables are configurable by “/specs/fetch_remote”
  Uses /data/cell_map file to determine a list of nodes from which it will fetch the following values
  Variables are automatically created
  Variables are automatically added to the “save_list”
  Spec file format – up to 20 variables
    #label data_type
    My_xzy REAL_TYPE
    My_int INT_TYPE
    My_logi LOGI_TYPE
    My_c STRING_TYPE
getAstStatGen