## Slide 1: Cyflex UPDATE – Feb 2023

## Slide 2: The information in this presentation is provided to all users of CyFlex. Please do not share this information to individuals not directly related to the use of CyFlex. Additionally, at lunch and learn events, there are multiple companies on this call and not all companies have non-disclosure agreements (NDA) with each other. Because of this, all participants should be careful to not share any proprietary information.”

## Slide 3: Agenda
Test Manager (gp_test)
  New gp_test keywords
  gp_header keyword format
  new tracing features
  gp_test speed improvement
  avoiding multiple restarts from “abort_limit”
NEW “cyflex_paths” feature
Review of “go.scp” preferred structure
Improvements to “delta_hst”

## Slide 4: KeywOrd - @PATH_OPTIONS
The @PATH_OPTIONS keyword provides a method for controlling the path of execution based on evaluation of computed expressions which must resolve to TRUE or FALSE
This is a “conditional” test to be evaluated at the beginning of a test mode much like @IF_TRUE, @IF_FALSE, @SWITCH. @PATH_OPTIONS will be evaluated after the other 3.
@PATH_OPTIONS
  #expression exit_path
  “my_logi && xyz” 100
  “my_logi && !xyz” 101
  ..etc… (up to 24)
If the “expression” evaluates to TRUE, then the “exit_path” is taken. The list is evaluated in the sequence as listed. If none evaluate TRUE, then other mode actions are executed.

## Slide 5: Keyword - @FASTBALL, @FASTBALL_FILE
The FASTBALL feature is designed to support very responsive updates to variables from a “furball” file by pre-reading the entire table into memory and assuming sequential access by index. If index not found by sequential access, defaults to search from the beginning of the table.
The FASTBALL keywords are a special case for launching the “vrbl_to_file” application in the READ_ONCE mode. There may be only one FASTBALL_FILE keyword per test procedure, but there may be more than one FASTBALL keyword (one per_mode).
  .

## Slide 6: @FASTBALL, @FASTBALL_FILE
The @FASTBALL_FILE keyword specifies the “furball” file and the index variable used to access the table values.
@FASTBALL_FILE
  #Success_path failure_path
  MODE_TERMINATE 99
  #pathname index_variable
  /specs/gp/vrbls/tc1 count
Each case of the @FASTBALL keyword is a reference to the file that has already been read into memory by the @FASTBALL_FILE keyword. The variables associated with the current index value are updated in memory.
@FASTBALL
  #success_path failure_path
  MODE_TERMINATE 99
  .

## Slide 7: @CHAIN_EVENTS
The @CHAIN_EVENTS keyword allows multiple processes to be synchronized in a fashion similar to @FUEL_READING_SYNC except that there is not necessarily any connection to taking a datapoint. The synchronization is handled externally from gp_test by a process named “chain_events”.
@CHAIN_EVENTS
  #input event output_event 1-shot delay
  In_ev_1 -
  In_ev_2 out_ev_1 1[sec]
  In_ev_3 -
  In_ev_4 final_ev
The specification consists of a list of input events, optional output events and optional 1-shot delays. Each output event is emitted when all of the input events listed on its line and all preceding lines have been received and 1-shots have expired

## Slide 8: @CHAIN_EVENTS
There may be up to 8 @CHAIN_EVENTS specifications in each test mode. Each mode that contains one or more @CHAIN_EVENTS keyword should contain a @CHAIN_EVENTS_ACTIONS keyword to specify the path to take when all of the input events have been received for each of the @CHAIN_EVENTS specifications.
Note that the input events can be received in any order. The output events are set only when all of the input events above it in the list have been received. An exception is for outputs specified with a 1-shot of IMMEDIATE, in which case the output event is emitted immediately when the input event is received.
An optional ‘display_string’ can be specified to show the pending inputs and active 1-shots
@CHAIN_EVENTS_ACTIONS
  #success_path display_string
  MODE_TERMINATE chain_names

## Slide 9: New “gp_header” file format
The header files is specified as an argument when launching 'gp_test’.
gp_test <filename> &
The default filename is '/specs/gp/gp_header', but each instance of gp_test must have a unique header file. Information in the header file uses keywords. With the exception of @INSTANCE, all keywords are optional, have default values, and may be entered in any sequence The first keyword must be @INSTANCE
@INSTANCE
test
When gp_test is launched it reads the header file and will create a new copy using the information in the current file plus all of the default values. It will contain all of the keywords, a description of each keyword and all of the default fields. The file is named /specs/gp/new_header.<name>. It can be copied over the original header file for subsequent use and modification. Do NOT reference the new file as an argument when launching gp_test. The following slides show the content of a “new” header file.

## Slide 10
Use a unique name for this instance - up to 31 characters
@INSTANCE
test
Priority for this instance - default is 16
@PRIORITY
19
Supply a label for an integer variable that will be used to display the current test mode
number. The default label will be test_mode_<instance name>
@MODE_NUMBER_LABEL
test_mode

## Slide 11
Supply labels for integer and string variables which will be used to display the procedure number and name of the current test procedure. The default labels will be test_num_<instance_name> and test_name_<instance_name>
@PROCEDURE_NUMBER_LABEL
test_num test_name_test
Supply a label for the 'countdown' variable which will be used to display the time remained until a mode times out. The default label will be countdown_<instance_name>
@MODE_COUNTDOWN
countdown

## Slide 12
Supply up to 4 string variable labels that will be used to display the mode descriptions of the current test mode and the previous 3 modes Default labels are:
TEST_DESC_<instance_name>
PREV_MODE1_<instance_name>
PREV_MODE2_<instance_name>
PREV_MODE3_<instance_name>
@MODE_DESCRIPTION_STRING_ARRAY
TEST_DESC PREV_MODE1 PREV_MODE2 PREV_MODE3
Supply the label of a string variable that will be used to display the current state of the stability specification if the @STABILITY_SPECS keyword was used in the current mode. The default label will be STABILITY_<instance_name>
@STABILITY_DESCRIPTION
STABILITY1

## Slide 13
Supply the labels of two string variables that will be used to display the event names associated with the @TERM_ALL_EVENTS keyword if the current mode contains that keyword. The first string will contain the event_names of input events that haven`t yet been received. The second label will contain the event name of the output event that has been set if all the input events have been received. The default labels will be TrmEV_waiting_<instance_name> and TrmEV_done_<instance_name>
@TERM_ALL_EVENTS_LIST
TrmEV_waiting TrmEV_done
Supply the labels of two string variables that will be used to display information associated with the @LIMIT_SPECS_ALL keyword if the current mode contains that keyword.
The first string will contain the names of unsatisfied limits that haven`t yet been received. The second label will contain the event name of the output event that has been set if all the input events have been received. The default labels will be TrmLIM_waiting_<instance_name> and TrmLIM_done_<instance_name>
@LIMIT_SPECS_ALL_STATUS
TrmLIM_waiting TrmLIM_done

## Slide 14
Tracing
max_lines: The maximum number of mode change entries per file
When this number of entries is reached,the file will be closed and a new trace file opened with the same base name and a new time stamp extender. Each time a particular instance of gp_test is started such as execution of a new go, a 'cleanup' operation is performed using the 'max_age' and 'max_files arguments for the 'cleanup' app.
max_age: The maximum age in days that will be used for the cleanup. Note that there may be older files present as the cleanup only occurs when this instance of gp_test is re-started.
max_files: The maximum number of files for this instance to be used for the cleanup operation refered to above.
When the number of mode changes reaches the maximum, the file is renamed to include a timestamp extender and a new <instance_name> file is opened.
The defaults are `-` 500 3 10
NOTE: the filename is no longer used, it defaults to the name of the instance
@TRACE_FILENAME
# 'name' max_lines max_age max_files
test 500 3 10

## Slide 15
Supply the label of a LOGICAL variable that can be used to enable or disable the gp_test trace output and the initial value of the variable (default is OFF for all instances except “test”). The value should be expressed as ON or OFF. The default label will be `gp_trace_<instance_name>`
@TRACE_ENABLE
gp_trace OFF

## Slide 16
Inserting the @ERROR_STRICT_ENFORCEMENT keyword means that a gp_test procedure cannot be started if there are errors detected when reading any procedure file.
@ERROR_STRICT_ENFORCEMENT

## Slide 17
The @UNIVERSAL_EVENTS keyword is used to direct control of the execution of gp_test to a test procedure when the specified event is received, regardless of which test procedure is currently being executed. However, if the same input event is specified as a @GLOBAL_EVENTS in the currently executing procedure, the path specified in @GLOBAL_EVENTS will take precedence.
You may specify up to 128 event/procedure lines in this file.There are no default specifications for this keyword, although the usual specifications would be to provide a response for the `emergency` event for the case of the gp_test instance which is managing the engine itself.
The gp_test instances which handle data acquisition systems, or auxiliary test cell systems should not have entries which manage engine shutdowns directly.
@UNIVERSAL_EVENTS
# event_name procedure
emergency /specs/gp/gp_emergency

## Slide 18
Registered events are special event messages which contain the name of a particular instance of gp_test for which the message is intended. There are a small number of such events and they listed below along with the user command which will send these events:
#event name user command
idle_mode idle
stop_test gp_stop
The @UNIVERSAL_REGISTERED_EVENTS keyword is used to direct control of the execution of gp_test to a test procedure when the specified event is received, regardless of which test procedure is currently being executed. However, if the same input event is specified as a @REGISTERED_EVENTS in the currently executing procedure, the path specified in @REGISTERED_EVENTS will take precedence.
You may specifiy up to 128 event/procedure lines in this file.
There are no default specifications for this keyword.
The gp_test instances which handle data acquisition systems, or auxiliary test cell systems # should not have entries which manage engine shutdowns directly
@UNIVERSAL_REGISTERED_EVENTS
# event_name procedure
stop_test /specs/gp/gp_shutdown
idle_mode /specs/gp/gp_idle

## Slide 19: “gp_test trace files”
The “gp_test” process will log mode changes to a trace file as configured to do so in the “gp_header” file using @TRACE_FILENAME and @TRACE_ENABLE keywords.
Trace files are written to the /specs/gp/trace/ directory
Traces for all instances are written to the same trace directory
The filenames in the trace directory begin with the instance name
The current trace messages will be written to a file using the name of the instance, such as ‘test’ or ‘smoke’.
When the maximum number of trace entries (max_lines) is exceeded, the file is renamed with a timestamp extender and a new base file is opened.
A “cleanup” operation is performed on the trace files each time an “nt” command starts a test. This is similar to the entries in the “usercron” file. The “max_age” and “max_files” parameters entered in the header file are used as arguments for “cleanup”.

## Slide 20: “gp_test trace file”
'1567593759' mode 0 terminated at- 09/04/19 06:42:39.575
nt command - /specs/gp/gp_wdl_SRC
gp_wdl_SRC,1 | Initialize Variables
'1567593769' mode 1 terminated at- 09/04/19 06:42:49.615
timeout - 10[sec]
gp_wdl_SRC,3 | Start Logger Task
'1567593769' mode 3 terminated at- 09/04/19 06:42:49.715
timeout - 0.1[sec]

## Slide 21: “gp_test trace file”
gp_wdl_SRC,5 :2/5000 | Start Logging and switch modes
'1567593769' mode 5 terminated at- 09/04/19 06:42:49.815
timeout - 0.1[sec]
gp_wdl_SRC,10 | Set Start Time
'1567593769' mode 10 terminated at- 09/04/19 06:42:49.815
immediate -
gp_wdl_SRC,14 | Read in setpoint info
'1567593769' mode 14 terminated at- 09/04/19 06:42:49.815
AUXILIARY_TASK - auRPL4a4f-114 - success

## Slide 22: “gp_test trace file”
gp_wdl_SRC,300 | Call return
'1567593769' mode 300 terminated at- 09/04/19 06:42:49.815
PROCEDURE called - return
return,10 | Test return
'1567593769' mode terminated at- 09/04/19 06:42:49.825
.01[sec] - RETURN to /specs/gp/gp_wdl_SRC

## Slide 23: GP_TEST speed improvement
When managing a loop that contained engine control commands such as @SPEED, @TORQUE, @SPD, @TRQ, @DYNO, @THROTTLE, if using the old “ctrl_task”, some delays were introduced so that loop times were not accurately determined by the mode timeouts.
When using the new “eng_ctrl_task”, “gp_test” does not suffer from this problem.
  .

## Slide 24: coming soon- new CYFLex paths feature
In March 2022, we received an email “inquiry” from Nathan Scott
Was thinking about trying to improve the file organization where we have test plans within the /esvd_data/$(gval tpid) directory instead of doing all of the symbolic linking as some systems are currently setup.
Basically, was trying to see how difficult it would be to allow cyflex programs to "base" in a different directory than or in addition to /specs for default spec file paths. For example, programs would first see if the default spec filename exists in /esvd_data/$(gval tpid) and then check specs. This would allow users to omit the full path and directly run things and work out of the /esvd_data/$(gval tpid) directory while still retaining /specs for everything else where the file doesn't exist within the test plan.
  .

## Slide 25: coming soon- new CYFLex paths feature
We have modified applications which read specification files to search for the ‘filename’ through a sequence of directories. The sequence of directories can be different for each installation (test cell). The applications uses the full pathname of the first match of ‘filename’ in the sequence. Each ‘translator’ app is modified to use this feature. This will not require changes to the applications for different sites or cells to support different selection sequences. A special command is used to specify the sequence of directories to be searched.
set_cyflex_paths /esvd_data/@tpid/ \
/esvd_data/$tpid/ \
/specs/ \
/cell/sub_systems/TestSystemIO/ \
/cell/ \
/cell/sub_systems/controls/
This is installed in the /cell/go.scp startup script after the “sys_start” and “error_mgr” commands.

## Slide 26: coming soon- new CYFLex paths feature
If set_cyflex_paths is installed, then the first path that has a match would take precedence. This would allow a user to have a default file in /specs/ and then copy it to /esvd_data/ if they want to use an edited copy.
Note that this design would allow a piecemeal implementation of translators to use the selection function and if ‘set_cyflex_paths’ is not specified in the go.scp, the system will work exactly as it does now. In other words, the rollout of this feature will have little impact for users who don’t use the path selection mechanism.

## Slide 27: coming soon- new CYFLex paths feature
Nathan’s example of how this would work:
Example 1:
/esvd_data/$tpid/pam_specs.abc (exists)
/specs/pam_specs.abc (exists)
Run: pam_specs pam_specs.abc (runs from esvd_data)
Example 2:
/esvd_data/$tpid/pam_specs.abc (not exists)
/specs/pam_specs.abc (exists)
Run: pam_specs pam_specs.abc (runs from specs)

## Slide 28: coming soon- new CYFLex paths feature
Example 3:
/esvd_data/$tpid/gp/gp_tranem (exists)
/specs/gp/gp_tranem (exists)
Run: nt gp_tranem (runs from esvd_data)
Example 4:
/esvd_data/$tpid/gp/gp_tranem (not exists)
/specs/gp/gp_tranem (exists)
Run: nt gp_tranem (runs from specs)